## Slide 1: Smart Control Systems

## Slide 2: Product line overview

## Slide 3: SoftPLC®
SoftPLC Programmable Automation Controllers (PAC’s)
  Functionality of PLC’s, RTU’s and DCS controllers combined with data/computation functions of computers
  All models include same features/functions and use same programming/maintenance software
  Models differ in hardware only (e.g.: ports, memory, speed)
SoftPLC Gateways (Protocol Converters)
  Any SoftPLC can be a Gateway
  Higher performance/more features than other gateway products

## Slide 4: SoftPLC
Industrial I/O
  Tealware™ - Modular rack-mounted I/O system, local & Ethernet configurations
  A-Series – Low count/low cost serial & Ethernet I/O
  Interface cards for industrial networks (e.g.: Profibus, DeviceNet)
TOPDOC® – SoftPLC Programming Software
  Configuration, application development, troubleshooting
  Available for Windows & Linux

## Slide 5: SoftPLC Web Studio
Web Studio is a complete SCADA software product
  All features included, no add-on costs
  Runs on any Windows environment, including mobile devices up to redundant servers
Web Studio HMI’s are Panel-PC’s w/ Web Studio runtime pre-loaded
  3.5” - 17” sizes available in standard models
  Custom sizes/specification models also available (e.g.: hazardous/marine area, other mounting options, etc.)

## Slide 6: Communication Products
Gatecraft Industrial Ethernet Products
  Switches/Routers
  Media converters
  Remote Access Modems
  Wireless Interfaces
  Firewalls/VPN’s
  Remote Serial Servers
Smart Netbox
Gatecraft Shield

## Slide 7: Company overview
1983
1988
1993
2001
2009
Tele-Denken formed
1st Release SoftPLC
Name change to SoftPLC
Linux Version SoftPLC
SmartBoard released
SoftPLC version Web Studio
Tealware I/O released
1996
2007
1985
1st Release SoftWires

## Slide 8: History – Key Events
Founded in 1983 as Tele-Denken Resources, Inc.
  By ex-Allen-Bradley employees
  Privately held, Texas Corporation
  US classified as small, woman-owned business
1980’s
  Driver interfaces between PC’s & PLC’s (O•N•E)
  A-B PLC programming software (TOPDOC®)
    for PLC/PLC-2, PLC-3, PLC-5
  A-B PLC emulation software (SoftWIRES™)
  A-B private-labeled TOPDOC PLC-3 as 6200 software

## Slide 9: History – Key Events
1990’s
  SoftPLC Controllers
  Tealware I/O
  Changed company name to SoftPLC Corporation
2000’s
  Gatecraft Linux O/S and Ethernet products
  SmartBoard & Smart product family
  SoftPLC Web Studio

## Slide 10: Corporate Strengths
Inventors & Innovators
  Many industry first software features/functions
  Embrace & provide open architecture technologies
  Apply computer technologies to industrial automation market
Focused market offering – specialize in industrial automation products
  Experts in embedded software (e.g.: I/O drivers, networking, operating systems)
  Reliability & Determinism comes first
Treasure customer feedback
  React quickly to customer requests

## Slide 11: Corporate Strengths
Excel in customer support services
  No “case numbers”
  Support staff are field experienced application engineers
  “I can’t remember a time in the last 20 years that a vendor went to the lengths that SoftPLC Corp. did to ensure our projects were a success.” (USACE)
Worldwide network of technical distributors & system integrators for local support
24-7/365 support available

## Slide 12: Customers
SoftPLC Customers can be found in a wide variety of industries world-wide
  Wood/Paper – Boise Cascade, Weyerhaeuser, Int’l Paper, Bowater...
  Food/Beverage –Safeway, Kraft, Pacific Shrimp, TeePak, Coca-Cola…
  Transportation – Ford, Detroit Diesel, GM, Schenck, Lockheed, Toyota…
  Quarries/Materials – Tilcon, LaFarge, Smurfit, Cadman…
  Power – USBR, Detroit Edison, Dracena, NW Natural Gas, SCADA Solns…
  Water – Ebasco, Taiwan Water, Miami-Dade County, City of Diamond IL…
  Pharma/Semi-Con – Quest Labs, Bayer, 3M, Panasonic, ThermoBiostar…
  PetroChem – BP, GE Plastics, China Petroleum, Shell, Dresser, Formosa…
  Metals –ArcelorMittal, Alcoa, Valesul Aluminum, Midwest Metals…
  and many more!

## Slide 13: Project Story
1996-ongoing: US Army Corps of Engineers
  Selected SoftPLC to replace old DCS system for hydroelectric controls after intense evaluation of controllers & I/O products
    Currently >300 PLC's for unit controls, fish mgmt, navigation locks…
    Each program ~10K rungs of logic, some have over 100K rungs
  Due to project success, SoftPLC was selected in 2009 for Grand Coulee Dam upgrade by US Bureau of Reclamation
    Largest power plant in the USA, 3rd largest in world (7GW)
    Also pumps water to irrigate eastern half of Washington state
    Using SoftPLC Web Studio HMI’s on this project too
  Combined, SoftPLC is used to generate over 5% of US power and 17% of US Hydropower

## Slide 14: Project Story
Nestle-Purina Pet Food 1997
  1st application replaced PLC-5 that wouldn’t communicate to serial weigh scale
  Replaced other PLC-5’s (all using existing 1771 I/O)
  Plant standard became SoftPLC for all new applications
    Despite Nestle standard of A-B

## Slide 15: Project Story
1995 Fonterra/Bonlac Foods/United Milk Tasmania
  PLC-5/80E out of memory & having comm problems
  Replaced CPU, connected to existing 1771 & SLC-500 I/O
  No changes to Citect SCADA required, comm problems fixed
  Added 3 Profibus networks

## Slide 16: SoftPLC PAC’s
Features/Functions

## Slide 17: “What is a SoftPLC?”
SoftPLC is control software that turns an industrial computer into an open architecture controller
  First “PAC” (Programmable Automation Controller) on the market
  Embedded software, runs on dedicated “headless” systems (eg: no monitor, keyboard…)
  Provides features of proprietary PLC’s (I/O control, PID) PLUS features of computers (flexibility, networking, speed)
Programming/Addressing modelled after A-B PLC’s
  A-B PLC “on steroids”
  Provides A-B users an easy, affordable upgrade path

## Slide 18: Market Positioning
SoftPLC’s are not PLC’s
  Better communications and data handling
  Advanced features – even beyond proprietary PAC’s
  Truly open architecture
SoftPLC’s are not PC-based controllers
  Deterministic scan (“hard” realtime)
  Online run-mode program changes
  Troubleshooting tools like PLC (Runtime Fault detection/ correction, I/O Forcing)
  Runs on embedded Linux, no Windows

## Slide 19: Hardware Models
Smart & Hardbooks for PAC/Gateway/Gatecraft

## Slide 20: SoftPLC’s SmartBoard®
All SoftPLC “Smart” products are based on the SmartBoard® design
SmartBoard provides rugged, compact, low-cost and powerful platform
  Customers can have common hardware for multiple product solutions
    Programmable Controls, Protocol Gateways, remote access modem, industrial firewall
  SmartBoard includes “hooks” for easy customization for OEM applications

## Slide 21: SmartBoard Hardware
Metal enclosure, DIN-rail mount
  Compact size (5.75”H x 6”D x 1.5”W)
Built-in managed Ethernet switch
  (2) IP interfaces for routing capability
  (4) RJ-45 10/100MB ports
  Fiber optic options on 1 port
(6) serial ports
  (1) 9 pin RS-232 interface
  (3) RS-232 ports
  (1) RS-485, 2-wire
  (1) factory configurable port (e.g.: Modem, RS-485 2/4 wire, A-B RIO)

## Slide 22: Smart SoftPLC I/O Interfaces
Selectable I/O interfaces
  Local Tealware Interfaces
    Backplane3 supports any 3 modules directly mounted on CPU
    LocalPorts supports up to 12 Tealware racks, up to 30’ from CPU
  Remote I/O
    Ethernet (e.g.: ModbusTCP)
    Serial (e.g.: Modbus)
    A-B RIO
  Bus I/O via PCI-104 interfaces (e.g.: Profibus, DeviceNet)
    Supports up to 3 interface cards

## Slide 23: Smart Environmental Specs
Low power requirement (2-5W based on options)
  14-48VDC or Power-Over-Ethernet
Industrially Rated:
  0~60oC operation, -20~85oC storage
    Extended temperature option available -20~70oC
  Humidity: 0~95% non-condensing
  Fanless/Diskless system
  Watchdog Timer
RoHS compliant

## Slide 24: SmartBoard Internals
Enet 1
LAN
Enet 2
LAN
Enet 3
LAN
WAN (PoE)
}
10/100MB ManagedEthernet Switch
Fiber Connector
(optional)
14~48VDC Power
SuperCap
~60 days battery-free RTC power
COM 2-4
RS-232
}
COM 1
(RS-232) “Console”
COM 6
Phone Modem,
RS/485, or other
serial to RJ-11 (eg: A-B RIO)
3.3V
PCI-104
Bus Interface
FPGA
63MB
SDRAM
20 pin
JTAG
(32) lines
FPGA I/O (3.3V)
+3.3 & 5V power
166MHz ARM9 CPU
(2) LED's tied to FPGA
}
4MB
Boot Flash
(5) GPIO
(3) FPGA I/O
}
SPI & 3.3V
25W sourcing P/S (12W in PoE mode)
COM 5
RS-485
(or A-B RIO)

## Slide 25: SmartBoard Internals
Compact Flash Interface (8 GBytes)
(future) SD Flash
}
133.35mm
149.09mm
(4) LED's for system control indication

## Slide 26: Hardbook Products
Powerful, stand-alone CPU’s
  Fanless, diskless
  Multiple Ethernet, serial, USB ports
  Up to 2GB RAM
Some models have PCI slot(s) for add-in cards
Many standard models
Custom versions available based on application requirements (ie: slots, form factor, communication ports, environmental)

## Slide 27: SoftPLC PAC’s
Firmware Features/Functions

## Slide 28: User Memory
Data Table Registers
  10K files of 10K elements each (100M words)
  Addressing similar to A-B PLC-5/SLC-500
    Binary, integer, floating point, PID, strings
    Timer, counter, arrays, more
  Status file for fault analysis, RTC, etc.
Every bit accessible by address or tag
Non-sequential display feature (Watch Window)

## Slide 29: User Memory
“Property Tables”
  Internal relational database
    Up to 10K tables of 10K elements each
  Ideal for use in sorting, recipe, warehouse applications
  Ladder instructions provided to read and process data records

## Slide 30: User Logic
Powerful Ladder Logic instruction set
  Over 135 standard functions
    Relay logic, timer/counter, math, data, PID, strings, more
    Similar to PLC-5/SLC-500 programming
  Program by address or tag
  Up to 10K subroutines of 10K rungs each
All logic documentation stored in SoftPLC

## Slide 31: User Logic
TOPDOC Loadable Modules (TLM’s) extend instruction set
  Created in C++ using toolkit, by SoftPLC Corp or customers
  Can be ladder instructions, drivers, or program tasks
Examples
  Calculations (Fourier transforms, cavitation, AGA gas flow)
  Device Interfaces (motion controller, I/O devices, PC cards)
  Encapsulate proprietary logic in a function block
  Read/write to database
  Print reports/Write files to remote disk

## Slide 32: User Logic
Some SoftPLC provided TLM’s:
  COMGENIUS – ASCII / Serial Communications
    Drives, bar code/RFID, weigh scales, process equipment
    Simple Modbus Master communications
  Log Data – Event Logging to CSV or binary formats
  Send Email/Text Message
    Includes support for attachments (e.g.: log files)
    Supports multiple recipients

## Slide 33: I/O Support
Supports up to 8K digital & unlimited analog
Up to 16 I/O drivers can be used simultaneously
Some available drivers
  Tealware local & remote I/O
  ModbusTCP Ethernet
  A-B RIO
  Industrial bus (e.g.: Profibus, DeviceNet, CANOpen, etc.)
  Serial I/O (Modbus & proprietary)
  PC bus I/O (e.g.: PCI, PCI/104 or direct CPU mounted I/O)
Third party driver development supported via toolkit

## Slide 34: Communications
Connection to SCADA/HMI, programming, peer-to-peer communications
  Multiple networks supported simultaneously
    Ethernet (A-B Enet, ModbusTCP)
    Serial (DF1, Modbus)
    Industrial Bus (e.g.; A-B DH+, Profibus)
  SoftPLC appears as A-B PLC-5 or Modbus device on the network
    All HMI/SCADA/DCS products supported
    OPC Servers supported

## Slide 35: Communications
Built-in FTP & SSH Servers
  Used to access SoftPLC flash disk files over Ethernet/serial ports
    Update/backup configurations, firmware, other files
    Low-level troubleshooting & diagnostics
    Access system logs
    Run command line programs
  Use any FTP/SSH client program

## Slide 36: Embedded Web Server
Optional firmware add-on module
Supports live pages in SoftPLC
  Pages update in real-time with application data
  Develop pages using any HTML editor
  Animation/data update can be done with C++, PHP, Python & other web technologies
View with any web browser

## Slide 37: Embedded Firewall
Optional firmware add-on module
Provides high-end protection and secure remote access
  Stateful inspection, NAT/IP masquerading, blacklisting
  Multiple VPN tunnels
  Ethernet & PPP protection

## Slide 38: Hot Standby/Redundancy
Optional firmware add-on module
Comprehensive solution for applications needing 100% uptime
  Bumpless transfer of I/O control in case of primary CPU fault
  High speed data transfer between primary/secondary controllers on dedicated Ethernet connection
    Uses “dumb” arbitrator to assist with switch-over
    Status available over network to SCADA/HMI, I/O, TOPDOC, other controllers
With Tealware I/O, fully redundant systems (CPU, I/O, P/S) possible

## Slide 39: Old PLC Upgrades
PLC-5, PLC-2/PLC, SLC-500, MicroLogix conversion services from SoftPLC
  Automated utility programs convert on average 95% of program logic and documentation
SoftLogix5, PLC-5/250 & PLC-3 conversion services quoted per application
  Semi-automated conversion process averages 85%
Other PLC conversions quoted per application
  Control/CompactLogix
  Schneider, Siemens, GE Fanuc

## Slide 40: SoftPLC Gateways
Configurable Protocol Converters & More….
Smart Gateway
Hardbook Gateway

## Slide 41: Flexibility
Up to 16 protocols per Gateway
  Supports multiple serial and Ethernet protocols
    All supported protocols always included – no need to order/stock different part numbers
    Select mix of master & slave protocols
  Industrial bus networks implemented via hardware add-on(s), base unit remains unchanged
Via Toolkit, users can add custom protocols

## Slide 42: Ports, Ports, Ports!
Minimum (2) Ethernet interfaces (MAC ID’s)
  Routing functions included
  Wireless and fiber options
Minimum (4) serial ports
Up to 8 industrial network interfaces (eg: Profibus, DeviceNet, etc.)

## Slide 43: Data / Throughput
No data limits
  100 Million 16-bit words per Gateway
Fastest Gateways on the market
  Highly optimized drivers
    Developed as PLC I/O drivers and/or PLC peer-to-peer communication

## Slide 44: Intelligence
Supports user logic for data manipulation
  Scaling, totaling, etc. via ladder logic
  Data logging to local flash and/or to network drives
  Email/texting functions can send alarms, data or data files as attachments
Great solution for data concentrator applications

## Slide 45: Security
Linux, FTP/SSH security by passwords
TOPDOC security
Firewall/VPN (firmware option)
  Protection of Gateway and connected devices from unauthorized access on any Ethernet or modem connection
  Remote access to Gateway data and configuration

## Slide 46: Diagnostics
All protocols provide detailed error reporting
User logic can automatically detect errors
  Report errors to attached SCADA/HMI
  Report errors via email/text messages
  Send peer-to-peer message to connected devices (if supported by device/protocol)
  Via connected I/O (optional) can issue alarms, modify machine/process behavior, etc.

## Slide 47: Control
Connected I/O and devices can be controlled by Gateway via ladder logic
  SoftPLC Tealware local I/O
  Serial (eg: Modbus)
  Ethernet (eg: ModbusTCP)
  Industrial bus (eg: Profibus, DeviceNet)

## Slide 48: Data Access
Any HMI/SCADA/DCS system can access Gateway data
  Ethernet or serial connection via standard PLC drivers
Toolkit enables user to write programs to read/write data over Ethernet
  Gateway can interface directly to databases (eg: SQL)

## Slide 49: Easy configuration
Easy to configure
  Configuration via Ethernet
  No programming required
    XML or text configuration files to map data from PLC/network address to internal Gateway address
  Free industrial bus network configuration / diagnostic software included with hardware interface(s)
TOPDOC is used as configuration and diagnostic tool

## Slide 50: Communication products
Smart Netbox, Other Gatecraft products

## Slide 51: Smart Netbox
Comprehensive “communications appliance”
  Industrial managed 4 port Ethernet switch/router
    Supports PoE (Power over Ethernet)
  Media converter (10/100BaseT to Fiber)
Remote Access Modem (w/ optional SM-MDM)
  Access any Ethernet device remotely via phone
  Lower cost & more powerful than competitor products
Industrial Firewall/VPN (w/ optional GC-FW firmware)
Remote Serial Server (w/ optional GC-SDS)

## Slide 52: Other Gatecraft Products
Product family name for all communication products
Firewalls/routers
  Gatecraft Shield - Ethernet to Ethernet protection
  Gatecraft Junction - Ethernet to Modem protection
  Gatecraft Beacon - secure WAP
Gatecraft Link - Ethernet switches & media converters
  Unmanaged, low-cost, DIN-rail options
    10/100, 10/100/1000, and fiber
  High-end switches (RuggedCom products)

## Slide 53: I/O
Tealware, A-Series, Other options

## Slide 54: Tealware I/O
Modular, high-density I/O system
  Local and remote Ethernet configurations supported
  Wide variety of digital, analog, & specialty modules
Easy to troubleshoot/maintain
  Detachable terminal block for easy replacement w/o re-wiring
  Diagnostic & Status LED’s
  Wide angle swing connector for easy installation
Digital modules hot-swappable under power

## Slide 55: Tealware I/O
Local interface to Smart SoftPLC or Smart Adapter
  3 modules per Backplane3 interface
  Connect to expansion racks via LocalPorts interface
    Up to 12 bases per Smart SoftPLC
    Up to 3 bases per Smart Adapter
Remote interface to any SoftPLC CPU via Ethernet
  Up to 255 drops per SoftPLC CPU
Modules fit into Rack Base
  6 or 8 module slot bases available
  Up to 10 feet between bases

## Slide 56: Smart Adapter
Decision making can be done at adapter level
  Define failure state based on process conditions
  Can take over as local controller if communication to master fails
  High level features (eg: remote decision making, SOE)
Embedded Firewall for security (w/ Cat No SM-FW option)
Network security increases with
Smart I/O Adapter/Switches

## Slide 57: A-Series I/O
Cost effective for applications requiring low count / small space / widely distributed I/O
  Serial RS-485 modules – over 90 signal types available
  Ethernet ModbusTCP modules – no adapter required, each module its own IP address
DIN-rail mount and modules can be stacked
    Sourced from multiple vendors as needed

## Slide 58: Other I/O Options
Using loadable drivers and appropriate hardware interfaces, SoftPLC CPU’s can communicate to other vendor I/O equipment
  Any ModbusTCP, Modbus
  Industrial buses (e.g.: Profibus, DeviceNet)
  PC bus cards, motion control interfaces
Via toolkit, additional drivers can be developed

## Slide 59: Configurations

## Slide 60: Backplane3 Configuration
BASE0x (Backplane)‏

## Slide 61: LocalPorts Configuration

## Slide 62: Example Configurations
I/O Modules
Ethernet
ModbusTCP
Smart Adapters
(Cat No SMS11-B)
Ethernet
ModbusTCP
Smart SoftPLC
(Cat No SMS11-B)
Hardbook SoftPLC
(Cat No HB-M0LE-x)

## Slide 63: Flexible!

## Slide 64: Bus I/O Configurations
Smart SoftPLC or Hardbook with Bus I/O
+
Profibus
ASI
DeviceNet
Interbus
CANOpen
SERCOS
etc.
Hardbook SoftPLC/Gateway
Bus Interface Card
(up to 8 cards)
+
Smart SoftPLC/Gateway
w/ PCI-104 bus option
PCI-104 Bus Interface Card
(Up to 3 cards)

## Slide 65: A-B RIO Configurations
Hardbook/Processor with A-B Remote I/O
+
1785-PKTX/PKTXD*
(Cat No SPO-PKTX)
1771-ASB
or other A-B RIO Adapter
Hardbook SoftPLC
(Cat No HB1-HPLA-x)
Smart SoftPLC w/ A-B RIO interface

## Slide 66: Allen-Bradley Upgrades with SoftPLC Controllers
THE Best Solutions
to upgrade A-B PLC's & HMI's
Minimizing cost, downtime, training & re-engineering

## Slide 67: A-B PLC Upgrades
Motivation:
    Product/programming software obsolescence
    Older technology lacks desired features/ communications
Why upgrade vs replace?
    Cost/downtime to replace entire system prohibitive
    I/O typically not an issue, only the CPU
“80% of end users surveyed were upgrading their control systems only, leaving field devices 'as is'.” Larry O'Brien, ARC Advisory Group

## Slide 68: A-B PLC Upgrades
              Models Supported
    PLC-5/SoftLogic5
    SLC-500/MicroLogix
    PLC-2, 1774 PLC
    PLC-3, PLC-5/250
Multiple I/O Types Supported
    RIO (eg: 1771, 1747, Flex, Block, etc.)
    DeviceNet, Profibus, etc. also supported via interfaces in SoftPLC CPU

## Slide 69: A-B PLC Upgrades
Process -
      Convert logic/documentation
      Replace A-B PLC CPU with SoftPLC Controller
  Existing I/O can remain virtually untouched
        Many options for future upgrades/expansion
  Existing HMI/SCADA can remain, if desired
  Existing communication networks can remain or be upgraded to Ethernet

## Slide 70: A-B PLC Upgrades
SoftPLC Hardware Options

## Slide 71: SoftPLC Hardware Options
Smart SoftPLC with A-B RIO interface
    Supports 2 RIO channels (32 adapters/channel)
    CPU includes Ethernet switch, multiple serial ports for DF1 or other protocols
DH+ available via external serial interface
RIO “blue hose” connection points

## Slide 72: SoftPLC Hardware Options
Hardbook SoftPLC w/ A-B Interface(s)
  Interface is via a PCI slot card
  1 or 2 port cards available
  Ports can be A-B RIO or Data Highway Plus protocol
  Up to 8 cards are supported by SoftPLC

## Slide 73: A-B PLC Upgrade Process
by PLC Model

## Slide 74: A-B PLC-5 Upgrades
SoftPLC logic/data table is a superset of the PLC-5
    Automated program conversion utility normally 98% or better (more of an import than a conversion)
      Resulting logic looks nearly identical to users
  HMI/SCADA does not normally need any changes (unless network type changes)

## Slide 75: A-B PLC-5 Upgrades
Hardware Changes
    Re-configure PLC-5 CPU as Remote I/O Adapter
    Add SoftPLC Controller w/ A-B RIO interface

## Slide 76: A-B SoftLogic5, PLC-5/250
Similar to PLC-5, but often text output needs to be “tweaked” before import
Add-on functions often need manual intervention, but can usually be supported with a SoftPLC TLM (loadable add-on) function

## Slide 77: A-B PLC-2 Upgrades
Automated conversion from PLC-2 logic to SoftPLC logic
    Program conversion normally 95% or better
    Converts from TOPDOC PLC-2 format
      Conversion cost includes loan of TOPDOC PLC-2 to upload program
  Documentation conversions available from most PLC-2 software programs
HMI/SCADA: SoftPLC has a PLC-2 compatibility mode to minimize changes required

## Slide 78: A-B PLC-2 Upgrades - Hardware
  PLC-2/30, -2/20, -2
      Replace PLC-2 CPU with SoftPLC Controller w/ A-B RIO interface
      If remote I/O, no changes required
      If local I/O, replace adapters with remote adapters (1771-ASB)
  Mini PLC-2's
      Replace PLC-2 CPU with remote I/O adapter
      Add SoftPLC Controller w/ A-B RIO interface

## Slide 79: A-B SLC-500 Upgrades
Automated conversion utility normally 95% or better
    Converts logic & documentation
      Provides text file identifying what conversion process did & any areas of concern
      Also provides equivalent Tealware I/O modules
  HMI/SCADA does not normally need any changes (unless network type changes)
  Resulting logic looks nearly identical to users (except for I and O addresses)

## Slide 80: A-B SLC-500 Upgrades
Hardware Changes (if keeping A-B I/O desired)
    Replace SLC-500 CPU with 1747-ASB remote I/O adapter
    Add SoftPLC Controller w/ A-B RIO interface
Or, replace entire system (if retaining IP the main desire)

## Slide 81: A-B PLC-3 Upgrades
Semi-Automated Conversion Utility
    Standard logic/documentation converts 90% or better
    Pointers, GA Basic, etc. must be manually converted (by user or SoftPLC can quote on per program basis)
    HMI/SCADA does not normally need any changes (if PLC-2 compatibility mode was originally used)
Hardware: Replace PLC-3 CPU w/ SoftPLC Controller w/ A-B RIO Interface

## Slide 82: A-B PLC Upgrades
Why SoftPLC
instead of A-B
Upgrade Solutions?

## Slide 83: Why SoftPLC vs A-B
A-B document on PLC-5 logic conversion is 80 pages
    53 pages (67%) discuss conversion “issues”, items that need to be manually reviewed, etc.
      27 pages (34%) are index, TOC, and instructions on export/import of logic and running the conversion utility program
SoftPLC list of issues is 1 page

## Slide 84: Why SoftPLC vs A-B
Resulting system more similar to old system
    Little training needed for maintenance personnel or operators
    Less risk of problems after conversion
Advanced features at no cost
    Ethernet/routing is standard feature
    Minimum user memory per SoftPLC is 64MB
    PAC functions standard (logging, email, internal database, Modbus/other drivers, more )
    More...

## Slide 85: Why SoftPLC vs A-B
Hardware Cost Savings
    Smart SoftPLC w/ A-B RIO interface $1500-$2500
    ControlLogix CPU, rack, P/S plus 1756-RIO minimum $7000
Common Solution for all applications
    Same SoftPLC products can range from smallest to largest applications (reduces inventory, training, software, etc cost)
    A-B has different products with unique physical structure such as I/O (MicroLogix, CompactLogix, ControlLogix)

## Slide 86: Why SoftPLC vs A-B
More options for future
  SoftPLC is open architecture, multiple choices of vendor for I/O, networks, drives, etc.
  Rockwell Automation solutions drive customer to all Rockwell products
Reduce automation costs long term

## Slide 87: SoftPLC Web Studio

## Slide 88: Web Studio Applications
Equipment Status
Real-Time Control
Data Acquisition/Reports
Recipes/Trends
Alarms
Control Room
Product Scheduling
Yields and Throughput
Quality Control
Statistics
Manufacturing
Enterprise
SCADA HMI
Web Studio spans applications from plant floor to control room to Enterprise.
HMI
SCADA

## Slide 89: Web Studio Overview
Real-time graphical interface to develop industrial automation, instrumentation, and embedded systems
  Over 150K installations world-wide in a wide range of applications and industries
Runs on any Microsoft Windows operating system
  Including mobile and embedded O/S
  Conforms to industry standards such as OPC, ODBC, XML, ActiveX

## Slide 90: Web Studio Functions
Object oriented graphic displays
Data logging & reporting, real-time & historical trending, alarms & recipe management
Tag database with a wide variety of data types
Programming via flexible scripting language
Automatic language translation
Multi-level application security
Web-Enabled to run applications in a browser

## Slide 91: Development Environment
Integrates seamlessly with other applications
  Windows desktop applications (e.g.: Word/Excel)
  3rd party packages (e.g.: C/C++, VB)
Online configuration, debugging
Extensive support tools
  Message register, error/event codes
  Database Spy
  LogWin
Context sensitive help

## Slide 92: Web Studio Features
Create stand-alone & web applications from the same development environment
Object oriented environment (screen/object re-usability)
  Powerful/flexible tag database with Boolean, real, string & array tags, classes & indirect pointers
  Advanced math library with >100 standard functions
  Programming via flexible/easy-to-use scripting languages

## Slide 93: Web Studio Graphics
Create sophisticated interfaces with point & click, drag & drop
Import graphics from >15 formats
Full-featured screen objects & dynamics with customizable properties
  Bar graphs, color, resizing, blinking, animation, scale, fill, positioning, rotation, commands, hyperlinks, combo-boxes, text input/output, and more
Extensive symbol library

## Slide 94: Web Studio Alarm System
Sophisticated alarms management system
  Send alarms to screen/email/browser
Free format alarm messages
Archive alarms to file, printer, or database
Filter, sort, or color sort alarms
  Filter by category

## Slide 95: Data Acquisition
Trending
  Keep track of process behavior online or via historical data
  Distribute information throughout network for easy monitoring on screens or web browsers
Recipes & Reports
  Create flexible, user-defined recipe groups
  Import/export recipes, reports & real-time data in XML, text or user-definable database formats
  Publish to web browsers

## Slide 96: Input/Output
More than 200 communication drivers to PLC’s, I/O & other devices/networks
  Supports OPC server & client
Conforms to industry standards (e.g.: .NET, OPC, ODBC, XML, SOAP, ActiveX)
SoftPLC Ethernet driver supports entire data table range

## Slide 97: Web Studio Products
Development Software
  Non-modular – all functions & drivers included
  Create applications for all target runtime hardware & O/S
Offered by tag count
  1500, 4K, 16K, 32K, 64K, unlimited
Combined Development/Runtime license available

## Slide 98: Web Studio Products
Runtime software
  Includes runtime & (1) each Web/Thin/SMA clients
  Additional clients can be added (up to 128/system)
Available for WinCE, Win Embedded, or Windows
Offered by tag count & number of communication drivers
Web Studio Runtime Licenses | 
150 tags, 1 driver | 16K tags, 5 drivers
300 tags, 1 driver | 32K tags, 5 drivers
1500 tags, 3 drivers | 64K tags, 8 drivers
4K tags, 5 drivers | “unlimited” tags, 32 drivers

## Slide 99: Web Studio HMI’s
Touchscreen Panel PC’s with Web Studio Runtime license factory installed
3.5” to 17” sizes available
  Customized sizes/environmental/packaging also available on request
All systems fanless, ruggedized hardware
Ethernet, serial & USB ports

## Slide 100: Thanks!
http://softplc.com
info@softplc.com